## Slide 1
PROBLEM
After harvest, straw needs a buyer and a baler
Source: Parali Se Paisa concept note; operational workflow shown later is a synthetic prototype.
1
A narrow window. Many fields. Scattered machinery and demand.
Farmers
Need a timely straw pickup option.
Operators
Need a clear dispatch queue.
Buyers
Need visible, traceable supply; this prototype does not establish actual demand.
Notes: Open with the practical coordination problem: residue has a short handling window; farmers, balers and buyers need a way to coordinate pickup. Our live evidence is satellite observation. The operating workflow is a prototype and uses synthetic records.

## Slide 2
SOLUTION
One evidence-to-action workflow
Source: application prototype; see README for real-data and synthetic-mode boundaries.
2
Observe
Sentinel-2 field histories
Prioritize
Normalized burn risk score, not probability
Coordinate
Demo baler/buyer workflow
Record
Prototype QR metadata check
REAL DATA → RULE-BASED INTERPRETATION → DEMO/SYNTHETIC OPERATIONS → PROTOTYPE RECORD
Notes: Explain the separation. Real mode is a read-only research view. The dispatch, buyer and evidence workflows are a separate synthetic prototype. No live service, verified registry, or incentive decision is claimed.

## Slide 3
REAL DATA
Muktsar map and one field history, 2023–2026
Source: fresh screenshots from isolated read-only real-data mode; 74 Sentinel-2 scenes, 12.6 million field-date observations; Fields of The World boundaries are model-derived.
3
74 Sentinel-2 scenes · 12.6 million field-date observations
REAL DATA · rule-based candidate map
REAL DATA · one field, stored observations
Notes: Show the district candidate map, then the selected field's dense satellite history. Missing dates are not interpolated. The field is an example, and the burn tiers are rule-based candidates, not independently validated labels.

## Slide 4
REAL DATA · RULE-BASED
Candidate area depends on the rule tier
Source: burn_candidate_summary.json and FINAL_JUDGE_EVIDENCE.md; full-revisit areas use non-overlapping 20 m pixels.
4
LOOSE_BURN_CANDIDATE
2023: 21,121 ha | 2024: 10,566 ha | 2025: 22,941 ha. Full-revisit, exploratory rule-based area.
STRICT_BURN_CANDIDATE
2023: 649 ha | 2024: 1,022 ha | 2025: 2,269 ha. Not a trend: haze/cloud changes clean pre-event coverage.
All outputs are RULE-BASED BURN CANDIDATES. Human review labels completed: 0.
Notes: The loose candidate area is exploratory and is the cross-season series shown. Strict area is precision-first but cannot be read as a year-to-year trend because clean pre-event coverage differs with haze and cloud. FIRMS/VIIRS is corroborative thermal context, not ground truth.

## Slide 5
DIFFERENTIATOR
Optical candidates and thermal context answer different questions
Source: 2025 strict-candidate / VIIRS matching analysis; defined ≤5-day evidence window; 500 m centroid radius.
5
8.8%
of 2025 strict optical candidates had a matched VIIRS active-fire detection within the defined window.
What the match means
About 9 in 10 strict optical burn candidates had no matched VIIRS active-fire detection within the defined matching window.
Interpretation
VIIRS is corroborative thermal context, not ground truth or a field-level confirmation.
Notes: In 2025, 8.8% of strict optical candidates had a matched VIIRS active-fire detection within the defined matching window. Say: About 9 in 10 strict optical burn candidates had no matched VIIRS active-fire detection within the defined matching window. Do not call this missed fires. Candidates are rule-based and VIIRS is corroborative thermal context.

## Slide 6
ACTION CONTEXT
A reported straw figure needs its source
Source: The Tribune, as cited in reference 11 of Parali Se Paisa Concept Note; news-reported estimate, not an official statistic.
6
12.1 lakh tonnes
The Tribune reported this straw estimate. It is not an official statistic.
From estimate to action
The product concept connects field evidence to straw pickup planning; actual supply and buyer demand still need field confirmation.
Attribution stays with the number wherever it appears: The Tribune (reference 11 in the concept note).
Notes: Attribute the 12.1 lakh tonne figure directly to The Tribune. It is a reported estimate and should not be represented as an official district statistic or as a measured result of our system.

## Slide 7
DEMO / SYNTHETIC
Dispatch is an operational prototype
Source: isolated local server, synthetic demo fixtures; route is a straight-line GEODESIC_PROXY only.
7
DEMO/SYNTHETIC · route proxy
PROTOTYPE · QR metadata only
Notes: Clearly label every object in this segment DEMO/SYNTHETIC. Routing is a straight-line geodesic proxy and does not provide road travel time. Baler and buyer records are fixtures, not verified registries.

## Slide 8
LIMITS
What the evidence can and cannot support
Source: FINAL_JUDGE_EVIDENCE.md; RESEARCH_SUMMARY.md; RESEARCH_METHODS.md.
8
No human validation yet
0 completed blinded labels
No strict trend
Pre-event clarity varies by season
No ground truth claim
Thermal matches are corroborative context
No probability claim
Risk is normalized score, not probability
Notes: We have not completed independent human labels. Strict and loose tiers are rule outputs. Risk is a normalized score, not a probability. Optical and thermal layers have different coverage limits. This is research decision support, not enforcement evidence.

## Slide 9
ACTION
Pilot the evidence-to-pickup loop
Project sources: docs/RESEARCH_METHODS.md; docs/PITCH_AND_DEMO_GUIDE.md; synthetic prototype workflow.
9
Real satellite evidence → clear limits → a prototype path from straw to value.
1 · Inspect
Muktsar real map and one field history
2 · Demonstrate
Synthetic dispatch and buyer workflow
3 · Pilot
Independent labels and local partners
Notes: Close by inviting the judges to inspect a real Muktsar field history, then show the separate synthetic dispatch and prototype QR metadata check. The next step is a bounded pilot with independent labels and real operator/buyer participation.